## Slide 1: Exactive Series API Introducing functionalities
Andreas Kühn
<erstellt von>

## Slide 2
Exactive Series API – What is it?
Application Programming Interface ( A P I )
This software component defines the communication between an
Exactive based instument and an user defined application.
As an interface between both, it exposes all accessible properties and functionalities of the instrument with the corresponding syntax of calls.
API

## Slide 3
Exactive Series API – What can you do with it?
Corresponding Interfaces

## Slide 4
Exactive Series API – What can you do with it?

## Slide 5
Exactive Series API – What can you do with it?

## Slide 6
To run your first application you will need:
+ Microsoft .NET ≥ 3.5
+ Development environment, like Visual Studio 2010/2012 (Express)
+ Latest Exactive Series Installation 2.3 (build 1765)
Getting started
C:\Xcalibur\system\Exactive\bin
API-1.0.dll
ESAPI-1.0.dll
(ESAPI-1.1.dll) – for offline method modification
Notes: Diffrences between VS 2010 Pro and express

## Slide 7
Include the interface by adding the two dlls to your references (VS)
Getting started
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 8
Getting started
Common Interface
Exactive Series extension
Central Access Point
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 9
This
Exactive Series API – Get connected (COM)
// Connect to the instrument
Type type = Type.GetTypeFromProgID("Thermo Exactive.API_Clr2_32_V1", true);
object o = Activator.CreateInstance(type);
IInstrumentAccessContainer container = (IInstrumentAccessContainer) o;
IInstrumentAccess instrumentAccess = container.Get(1);
Central Access Point
Instrument Number
IExactiveInstrumentAccess exactiveAccess =
instrumentAccess as IExactiveInstrumentAccess
The central access point is the IInstrumentAccessContainer which serves as a master to get access to all other interfaces in this namespace and all contained namespaces.
Different access for SW > 2.6, please check ExactiveApiUsageExample 1.0 for details.
Notes: The string Thermo Exactive.API_Clr2_32_V1 is the ProgId in terms of COM to access the implementing class type.
The use of the Activator is the .NET way to create an instance of the implementing class and in the next line the desired interface IInstrumentAccessContainer is
pulled out of the implementing class. Of course, standard COM techniques can also be used with COM's IUnknown::QueryInterface and so on.

## Slide 10
Getting started
Scan Data/Information
Contol of the instrument
Analog Traces like from UV-Detectors
Basic access to the instrument
Central Access Point

## Slide 11
InstrumentAccess
Control Interface
Acquisition
SetScans
Method
Access rights; what user role is currently set and what user roles are accessible
Error Messages from instrument
Data Container
Still connected?
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 12
ExactiveAccess
using Thermo.Interfaces.InstrumentAccess_V1;
using Thermo.Interfaces.ExactiveAccess_V1;
IExactiveInstrumentAccess exactiveAccess;
exactiveAccess.UserRolesChanged += new EventHandler(access_UserRolesChanged);
Namespaces
Register to an event, that is fired if
the CurrentUserRole is changing
private void access_UserRolesChanged(object sender, EventArgs e)
{
SetText(exactiveAccess.CurrentUserRole.ToString(), userRoleStatus);
}
Reacting on event (e.g. output new user role to a GUI)
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 13
Getting started
Scan Data/Information
Basic access to the instrument
Central Access Point
Contol of the instrument
Analog Traces like from UV-Detectors
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 14
MsScanContainer
Where is it coming from
Last Scan Information
RAW file Acquisition
Started or stopped
(EVENT)
NEW scan has arrived (EVENT)
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 15
private void msScanContainer_MsScanArrived(object sender, MsScanEventArgs e)
{
AnalyzeScan(e.GetScan()); // will analyze the scan data of the arriving scan
}
MsScanArrived (EVENT)
msScanContainer = instrument.GetMsScanContainer(0);
msScanContainer.MsScanArrived += new EventHandler<MsScanEventArgs>(MsScanArrived);
Register To MsScanArrived EVENT
Get direct access to scan data, when event is fired
Without influencing the scan speed of the instrument, you can access the data of each arriving scan directly via the passed event arguments. The obtainable IMsScan interface will let you access all the data (using a link to the corresponding location in shared memory)
Multiple Instances can register to the same events and will be all notified
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 16
IMsScan
Are there Centroids at all? (NULLABLE)
Spectral Data (Centroids)
ScanProperties
(common)
Access To Profiles
ScanProperties
(specific)
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 17
ICentroid
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 18
Getting started
Scan Data/Information
Basic access to the instrument
Central Access Point
Contol of the instrument
Analog Traces like from UV-Detectors
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 19
IAnalogTraceContainer
Last Data Point
Last Scan Information
Update Frequency (nullable)
NEW Trace Point has arrived
e.g. UV Trace
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 20
Getting started
Scan Data/Information
Basic access to the instrument
Central Access Point
Contol of the instrument
Analog Traces like from UV-Detectors
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 21
IControl
Create an instance of the IScans Interface to take over the instrument control e.g. to set customized scan definitions
This can be done exclusively (no other instrance is allowed) or non-exclusively.
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 22
Scanning Level
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 23
IScans
Create a Customized Scan Definition
Scanning Level
Tells you, when the instrument is ready to
take another scan definition to execute.
Event timing is coordinated to keep the
instrument doing ion injection and transient
acquisition in parallel
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 24
IScans – Example to define a scan
private void SetMS2Scan(double mz)
{
  ICustomScan cs = scansControl1.CreateCustomScan();
  cs.RunningNumber = 4000;
  // Allow an extra delay of 500 ms, we will answer as fast as possible
  cs.SingleProcessingDelay = 0.50D;
  cs.Values["IsolationRangeLow"] = (mz - 2).ToString();
  cs.Values["IsolationRangeHigh"] = (mz + 2).ToString();
  cs.Values["FirstMass"] = "50";
  cs.Values["LastMass"] = "1000";
  cs.Values["Polarity"] = "0";
  cs.Values["NCE"] = "27";
  cs.Values["Resolution"] = "17500";
  scans.SetCustomScan(cs)
}
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 25
IScans
Wait up to „ProcessingDelay“ for new customized scan definition (e.g. up to 500ms). CancelRepetition can cancel wait state
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 26
Scanning Level – set a repeating scan def.
private void setRepScanDef()
{
  IRepeatingScan repS = scans.CreateRepeatingScan();
  repS.RunningNumber = 2;
  repS.Values.Add(“Resolution", “140000");
  try
  {
  scans.SetRepetitionScan(repS))
  }
}
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 27
API – Example: asynchronous approach of analyse and contol
CANDIDATES
829.43359
415.22165
732.38275
.
.
.
Analyze Full MS scan and fill candidate list
Get best candidate

## Slide 28
API – Example – TopN (extract)
using Thermo.Interfaces.InstrumentAccess_V1;
using Thermo.Interfaces.InstrumentAccess_V1.MsScanContainer;
using Thermo.Interfaces.InstrumentAccess_V1.Control;
using Thermo.Interfaces.InstrumentAccess_V1.Control.Scans;
// connect to instrument
Type type = Type.GetTypeFromProgID("Thermo Exactive.API_Clr2_32_V1", true);
object o = Activator.CreateInstance(type);
IInstrumentAccessContainer container = (IInstrumentAccessContainer) o;
IInstrumentAccess instrumentAccess = container1.Get(1);
// get the scan container
IMsScanContainer msScanContainer = instrumentAccess.GetMsScanContainer(0);
// create a IScans instance (non-exclusively) to execute customized scans
IScans scansControl = instrumentAccess1.Control.GetScans(false);
// register to events…
// listen to the scan data stream
msScanContainer.MsScanArrived += new EventHandler<MsScanEventArgs>(checkScans1);
// syncronize the deployment of scan definitions to stay in parallel (inject, transient)
scansControl1.CanAcceptNextCustomScan += new EventHandler(scans_CanAcceptNextCustomScan);
Namespaces
Access to instrument, Listen to data stream, synchronize scan deployment

## Slide 29
API – Example – TopN – get candidates out of MS1 scans

## Slide 30
API – Example –TopN -select a candidate for a scan or do MS1

## Slide 31
Icontrol – Acquire Raw Files
Acquire Raw Files
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 32
IControl
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 33
IControl

## Slide 34
Acquisition

## Slide 35
Icontrol – Acquire Raw Files
Method related functionality
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 36
IControl – modify tables at runtime
Create a table of the passed type. (IInclusionTable, IExclusionTable)
The created table can be used to call ReplaceTable(Int32, Int64, ITable).
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 37
IControl – modify tables at runtime
Load a table of the passed type with the specified table index
from a named method file.
Returns null if the table was not found, otherwise the table filled with found items.
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 38
IControl – modify tables at runtime
Replace a table currently used by the instrument.
Returns true if the command has been sent to the instrument, false otherwise
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 39
IControl – Example (extract)
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 40
IControl – IExactiveControl
ESAPI-1.0.dll
ESAPI-1.1.dll
Additional functionality for IExactiveControl interface. (Exactive Series specific)
The returned IMethodEditor instance allows direct manipulation of a method.
Method's content can be stored back to an IStorage interface or byte buffers
Notes: Two dlls: 1) common functionalities, that are valid for all instruments 2) instrument specific functionalities

## Slide 41
IControl – Manipulate methods
Available global properties
Get a specific table of
the method
Store modified table
Store the method‘s content
Currently we are allowing
only the manipulation of
tables and changing of the
method‘s runtime.

## Slide 42
API - Portal
1. Create an account by entering the website shown below and click “Create an account”.

## Slide 43
API - Portal
2. Please fill out the “Registration” form and use “Exactive Series API” as “Primary Software Interest”. Please use a valid and traceable email address and don’t forget to accept the “Terms & Conditions”.

## Slide 44
API - Portal
3. Wait for an registration email and use the corresponding activation link to for this portal.

## Slide 45
API - Portal
4. You will receive another email, that your account has been approved and you are promoted to the IAPI area. As we need to check the contact data and compare it with a list of people that have been defined as potential users:
THIS COULD TAKE SOME HOURS - UP TO SOME DAYS (at weekends).
NO RESPONSE AFTER 3 WORKING DAYS -> PLEASE CONTACT ME AGAIN